Rev. B/C
X-Extruder Harness
- *No strain-relief teeth on mounting brackets!*
- *Cut X-min endstop wires 80mm not 40mm!*
- Heatshrink Z-max endstop wires together
- Make extruder motor cable 1150mm long
- Increase strip length for ferrite to 150mm (bring ferrite back 50mm)
- Shorten X-min/Z-max cable to 720mm
- Shorten X motor cable to 720mm
- Increase strip length of 20 position connector to 60mm
- Label wires

Bed Harness
- Increase Y-endstop cable strip length to 60mm
- Increase bed power cable strip length to 50mm
- Reduce the Z-probe cable length to 670mm, reduce the left strip length to 190mm
- Cut 40mm off the diode wire
- Label wires
Rev. D
X-Extruder Harness
- *No strain-relief teeth on mounting brackets!*
- *Cut 80mm off X-min endstop wires, not make it's length from the jacket 80mm!*
- Fix X-Motor label (X, not Z)
- Increase left-side E-Motor strip length to 80mm
Double-Ferrite X-Extruder Harness
Increase left side strip length to 170mm and move ferrites to that new farther strip edge

Bed Harness
- *No strain-relief teeth on mounting brackets!*
- *Cut 40mm off brown diode wire, not make it's length from the jacket 40mm!*
- Increase right-side Y-Endstop cable strip length to 75mm
- Move labels to 25mm away from the pin